SPECIFICATION FOR MT – 263020/TRH/A

RHCP READER ANTENNA

902-928 MHz, 11 dBic

| REVISION RECORD |
| --- |
| DATE | APVD | DESCRIPTION | ECO | REV |
| 25.6.06 | YAEL H. | RELAESED | CV92 | A |
| 12.4.07 | YAEL H. | UPDATE 3 dB BEAMWIDTH | 2083 | B |
| 18.4.12 | YAEL H. | UPDATE ANTENNA DIM | 5579 | C |

| 56 | 55 | 54 | 53 | 52 | 51 | 50 | 49 | 48 | 47 | 46 | 45 | 44 | 43 | SHEET |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | REV |
| 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32 | 31 | 30 | 29 | SHEET |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | REV |
| 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | SHEET |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | REV |
| 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | SHEET |
|  |  |  |  |  |  |  |  |  |  | C | C | C | C | REV |

| PRODUCT STATUS: |
| --- |
| PRODUCTION | PREPRODUCTION | IN DEVELOPMENT | PROPOSAL |

| CONTRACT NO |
| --- |
| DATE | SIGN | NAME | ACTION |
| 1.6.06 | YAEL | YAEL HARASH | PREP |
| 22.6.06 | D.F | DOV FEINER | CHKD |
|  |  |  | CHKD |
|  |  |  | CHKD |
| 4.6.06 | H.A | ASAF HAVIV | DSGN |
| 4.606 | A.D | ALEX DRAGILEV | PROJ |
|  |  |  | MFG |
| 5.6.06 | MOTI | MOTI MOTOVICH | QA |
| 11.6.06 | D.S | DAVID SHANI | MARK. |

SPECIFICATION

FLAT  PANEL  READER  ANTENNA

| MTI PART NUMBER | MT – 263020/TRH/A |
| --- | --- |
| REGULATORY COMPLIANCE | RoHS , CE 0682 |
| 1. ELECTRICAL |  |
| FREQUENCY RANGE | 902 - 928 MHz |
| GAIN | 11 dBic (min) |
| VSWR | 1.5:1 (max) 1.3:1 (typ) |
| AZIMUTH 3 dB BEAMWIDTH | 30( (typ) |
| ELEVATION 3 dB BEAMWIDTH | 63( (typ) |
| POLARIZATION | RHCP |
| SIDELOBES LEVEL | -12 dB (max) -15 dB (typ) |
| AXIAL RATIO AT 3 dB BEAMWIDTH | 3 dB (max) |
| F/B RATIO | -20 dB (max) |
| INPUT IMPEDANCE | 50 (ohm) |
| INPUT POWER | 6 W (max) |
| LIGHTNING PROTECTION | DC Grounded |
| 2. MECHANICAL |  |
| DIMENSIONS (LxWxD) | 650x320x32 mm (max) |
| ORIENTATION | Rectangular |
| WEIGHT | 2.8 Kg (max) |
| CONNECTOR | TNC Reverse polarity |
| RADOME | Plastic UV Resistant per ETSI 300 |
| OUT LINE DRAWING | RD41895600C |
| 3. MOUNTING KIT | SEE RD41191800C, MT-120019 |

| 4. ENVIRONMENTAL |
| --- |
| TEST | STANDARD | DURATION | TEMPERTURE | NOTES |
| LOW TEMPERATURE | IEC 68-2-1 | 72 h | -55°C | - |
| HIGH TEMPERATURE | IEC 68-2-2 | 72 h | +71°C | - |
| TEMP. CYCLING | IEC 68-2-14 | 1 h | -45°C +70°C | 3 Cycles |
| THERMAL SHOCK NONO-OPERATING |  |  | -30°C to +70°C | Ramp 30°C/min |
| HUMIDITY | ETSI EN300-2-4 T4.1E | 144 h | - | 95% |
| WATER TIGHTNESS | IEC 529 | - | - | IP54 |
| DUST RESISTANCE |  |  |  | IP54 |
| SOLAR RADIATION | ASTM G53 | 1000 h | - | - |
| OZONE RESISTANCE | ETSI 300 |  |  |  |
| FLAMMABILITY | UL 94 | - | - | Class HB |
| SALT SPRAY | IEC 68-2-11 Ka | 500 h | - | - |
| QUASI RANDOM VIBRATION |  |  |  | 20g rms for 4 hours |
| VEHICLE VIBRATION OPERATING | 1g rms, 10-500 Hz, in 3 axis |  |  | 6 hours total, 2 hr in each axis. Accelerated wear – an additional 50hrs in worst case axis. |
| MECHANICAL SHOCK OPERATING | 10g, 11 msec, half sine pulse |  |  |  |

# Text boxes

THIS DOCUMENT AND THE INFORMATION CONTAINED IN IT ARE PROPRIETARY AND CONFIDENTIAL TO MTI.  NO PERSON IS ALLOWED TO COPY REPRINT REPRODUCE OR PUBLISH ANY PART OF THIS DOCUMENT NOR DISCLOSE ITS CONTENTS TO OTHERS NOR MAKE ANY USE OF IT NOR ALLOW OR ASSIST OTHERS TO MAKE ANY USE OF IT, UNLESS BY THE PRIOR WRITTEN EXPRESS AUTHORIZATION OF MTI AND THEN ONLY TO THE EXTENT AUTHORIZED.

# (C) COPYRIGHT – MTI WIRELESS EDGE LTD.